## Slide 1: AI based Network Management Agent (NMA): Concepts & Architecture
AI based Network Management Agent: Industry Direction and Standards Opportunities
Presenters:
Daniele Ceccarelli (Cisco)
Xing James Jiang (Cisco)

## Slide 2: draft-zhao-nmop-network-management-agent/
Background
Draft linked and presented many times in NMOP working group
Scope
  This draft establishes a standardized architecture for AI Agents in Network Management (Network Management Agents - NMAs).
  Goals
Define the foundational framework of the NMA.
Clarify the relationship between the NMA and existing network controllers.
Specify functional requirements for NMAs across various network scenarios, including their required interfaces.
Not Goals
Specific agent implementation details are out of scope.
Draft authors:
Xing Zhao (CAICT)
Minxue Wang (CMCC)
Bo Wu (Huawei)
Daniele Ceccarelli (Cisco)
Haomian Zheng (Huawei)
Jin Zhou (ZTE)

## Slide 3: NMA definition
NMA = AI Agents for network management = A network management entity built on ML/AI and equipped with the processing capabilities to create autonomous closed-loop.
It interacts with other components of the NM tools to: carry out network perception, do task intent interpretation, task planning, decision-making and task execution operations based on user task intentions or preset goals, so as to achieve closed-loop operations
Decisions
Action
Insight
NMA
Not replacing existing tools!!!

## Slide 4: Relationship with RFC8969
RFC 8969 A Framework for Automating Service and Network Management with YANG
Relation: this draft enhances RFC 8969 with AI/ML “intelligent” capabilities
Layering and Representation withing a network operator
NMAs
NMAs
Enhanced intelligent network management and control framework based on NMA
Orchestrator
NMAs
Service Modeling
Service Orchestration
Controller
NMAs
Network Modeling
Network Orchestration
Device
End-side AI
Device Modeling
NMAs
NMAs
NMAs
NMAs
Inter-layer
A2A interface
Intra-layer A2A interface
NMA1
NMA2
Hierarchy NMA interaction
NMA can exist at both the Controller and Orchestrator levels.

## Slide 5: NMA interfaces – impacts of deployment models
Extended model
Integrated model

## Slide 6: NMA interfaces – CHALLENGES AND OPPORTUNITIES
NMA Agentic Framework
Multi agent support
NBI
Agent operations
LLM proxy&routing
LLM
Inter agent comm.
External NMA
Data retrieval
Network
Controllers
Data Lakes
Knowledge Graph
Knowledge Graph
+ Building trust !!!!!

## Slide 7: CHALLENGES AND OPPORTUNITIES
Standardization opportunities
  Interfaces:
    NBI (including NMA operations and NMA usage)
    Agent to Agent (specific for NMA?)
    Data collection (MCP? MCP for NMA?)
  Are the industry protocols good enough? E.g. MCP, A2A vs A2A-T ?
  Knowledge graph internal or external? Need for a standard way to feed it (NMOP)
  Trust: a standardized way of measuring agent reliability/trustworthiness

## Slide 8: THANK YOU

## Slide 9: HOW the deployment mode impacts NMA interfaces
Mode a): Independent Mode
Mode b): Integrated Mode
NMA is independent from the original controllers.
  A new east-west interface (A2C) needs to be added between NMA and controller to achieve capability calling and result feedback.
  An intelligent southbound interface ( “A2N”) needs to be added between NMA and the physical network.
  NMA interacts with users (human or other agents) through a new A2U interface (A2A interface belongs to the scope of this interface)
  NMA is integrated and serves as a function of the controller.
    NMA interacts with original function modules through internal A2C interface.
    NMA interacts with users through extended NBI (including A2U)
    The enhanced MCS interacts with underlay physical network through extended SBI (including A2N)