## Slide 1: Deutsche Telekom Use Case: Unexpected Incidents with Multi-Agent Collaboration
IETF 125 Shenzhen, March 2026

## Slide 2
Unexpected Incidents Scenarios and Challenges
Scenarios
Marathons
Traffic Jams
Traffic Burst and Performance Degradation caused by Large number of User Access
Challenge 2: Manual Optimization is Low-efficiency for Experience Assurance/Compliant Handling
Hour-level traffic monitoring cannot capture the traffic burst occur at minute-level
9:00
Burst traffic
10:00
Hour
Load traffic statistics
11:00
12:00
Offline Tools
Data collection
Issue analysis
Solution formulation
Review and delivery
Automatic processing
Manual handling
Hours / Days
Challenges
Challenge 1: Perception and Prediction of Traffic Burst
Scenario1
Un-planned Events
Scenario2
Planned Events
Typical Event | Accidents/Traffic Jams/... | Concerts/Sporting/…
Characteristics | unfixed time & location | Fixed time & location
Suggestion | Focus on Downlink throughput optimization | Focus on Uplink throughput optimization
Sport Events

## Slide 3
DT Agentic Architecture
Network
Layer
Service
Layer
Principal Agent
Service Task Agent 1
(e.g. RAN Guardian)
Service Task Agent 2
…
Domain 1
Task Agent
Domain 2
Task Agent
…
Achieve single domain autonomy
Collaborate with multi-vendor and multi-domain agents
DT Agentic Architecture
Introducing agents at both service layer and network layer: Multi-vendor and multi-domain autonomy enabled by single domain autonomy

## Slide 4
Download Speed<5Mbps
Percentage*
~6%
TO-BE
AS-IS
Service Experience Promotion enabled by Collaboration of Multi-layer agents
Network Optimization Agent
NEM
NE
DTRC
Event Scan
Opt. Policy
Decision & execution
DT Guardian Agent
Internet data
Guardian Target
Guardian Policy Decision
Effect Evaluation
Operation Team
Traffic Prediction
Traffic Burst Detection
Traffic Burst Optimization
Intra-frequency
Inter-frequency
RF,MLB,HO,…
Complaint
User Experience
Before Event
During Event
After Event
↓ Intent Generation
↑ Monitor and Predict
↓ Policy & Conflict decision
↑ Opt. Policy Suggestion
↓ Business Eva.
↑ Network Eva.
Agent-to-Agent Communication
Scenarios
Values
Realtime Perception
1-2 Hours
Minutes detection
AS-IS
TO-BE
Hours
foresight
Realtime Optimization
3 -4 Hours
Minutes
AS-IS
TO-BE
Planned Events: 1500+ Events in Germany per year. for example, Beer Exchange, Concerts, Sports in the venue.
Un-planned Events : traffic-jam, cell out-of-service.
Planned Events
Un-planned Events
Service
Layer
Network
Layer

## Slide 5
Discussion